## Slide 1: KM5 Business Processes – 2 Day Overview
Introduction / Overview of key legislation and standards
Health & Safety
Handling Materials: WEEE, COSHH & RoHS
Handling Data: DPA, FoI, CMA, RIPA
Business Continuity
IT Strategy
IT Systems
Professional Development
Life Cycles

## Slide 2: Legislation, Regulations, Standards and Codes of Practice

## Slide 3: Contents
Health and safety at Work Act 1974
Electricity at Work Regulations 1989
Control of Substances Hazardous to Health 2002 (COSHH)
Restriction of Substances Hazardous to Health (RoHS)
Waste Electrical and Electronic Equipment Directive (WEEE)
Standards

## Slide 4: Health and Safety at Work Act 1974
What is the Health and Safety at Work Act 1974?
Also known as HASAW or HSW
UK Health and Safety Legislation
Employers need to ensure the health, safety and welfare at work of ALL their employees
Why does it exist?
To address fundamental issues of workplace safety
To comply with the Law of the European Union
What responsibilities do employees have when complying with HASAW?

## Slide 5: Health and Safety at Work Act 1974
What is the Health and Safety at Work Act 1974?
Also known as HASAW or HSW
UK Health and Safety Legislation
Employers need to ensure the health, safety and welfare at work of ALL their employees
Why does it exist?
To address fundamental issues of workplace safety
To comply with the Law of the European Union
What responsibilities do employees have when complying with HASAW?
Take reasonable care for the health and safety of him/herself and of other persons who may be affected by his/her acts or omissions at work; and
Co-operate with employers or other persons so far as is necessary to enable them to perform their duties or requirements under the Act.

## Slide 6: Health and Safety at Work Act 1974
Duties of persons in general
Section 8 of the Act requires that "no person shall intentionally or recklessly interfere with or misuse anything provided in the interests of health, safety or welfare in pursuance of any of the relevant statutory provisions."

## Slide 7: Health and Safety at Work Act 1974
What does HASAW cover?
It covers Occupational Health and Safety in Great Britain
Agriculture (safety, Health and Welfare Provisions) Act 1956
Employment Medical Advisory Service Act 1972
Employment of Women, Young Persons, and Children Act 1920
Environment and Safety Information Act 1988
Explosives Act 1875
Factories Act 1961
Health and Safety at Work etc Act 1974
Health and Safety (Offences) Act 2008
Mineral Workings Offshore Installations Act 1971
Mines and Quarries (Tips) Act 1969
Mines and Quarries Act 1954
Offices, Shops and Railway Premises Act 1963
Offshore Safety Act 1992
Pipe-lines Act 1962

## Slide 8: Health and Safety at Work Act 1974
What is the difference between an Act, a Regulation, a Standard, a Code of Practice, and a Directive?
An Act is Law passed by a higher official body such as the House of Lords
A Regulation is a rule or directive made and maintained by an authority.
A Directive is an official or authoritative instruction
A code of practice is a set of written rules which explains how people working in a particular profession should behave

## Slide 9: Electricity at Work Regulations 1989
Electricity at Work Regulations 1989
What is it?
It aims to highlight what can be done by duty-holders(1) to achieve electrical safety compliance.
It is relevant to all work activities and premises
It is also of interest and help to engineers, technicians and their managers
1 owner of the non-domestic premises or the person or organisation that has clear responsibility for the maintenance or repair of non-domestic premise
What is its purpose?
The purpose of the Regulations is to require precautions to be taken against the risk of death or personal injury from electricity in work activities.

## Slide 10: Electricity at Work Regulations 1989
Electricity at Work Regulations 1989
What does it cover?
Systems, work activities and protective equipment
Strength and capability of electrical equipment
Adverse or hazardous environments
Insulation, protection and placing of conductors
Earthing or other suitable precautions
Integrity of referenced conductors
Connections – plugs and sockets
Means for protecting from excess of current
Means for cutting off the supply and for isolation
Precautions for work on equipment made dead
Work on or near live conductors
Working space, access and lighting
Persons to be competent to prevent danger and injury

## Slide 11: Control of Substances Hazardous to Health 2002 (COSHH)
Control of Substances Hazardous to Health 2002 (COSHH)
What is it?
COSHH is the law that requires employers to control substances that are hazardous to health and includes nanomaterials
What is its purpose?
To prevent or reduce workers' exposure to hazardous substances by
-finding out what the health hazards are;
-deciding how to prevent harm to health (risk assessment);
-providing control measures to reduce harm to health;
-making sure they are used;
-keeping all control measures in good working order;
-providing information, instruction and training for employees and others;
-providing monitoring and health surveillance in appropriate cases;
-planning for emergencies

## Slide 12
Control of Substances Hazardous to Health 2002 (COSHH)
What does it cover?
chemicals
products containing chemicals
fumes
dusts
vapours
mists
nanotechnology
gases and asphyxiating gases and biological agents (germs). If the packaging has any of the hazard symbols then it is classed as a hazardous substance.
germs that cause diseases such as leptospirosis or legionnaires disease and germs used in laboratories
Control of Substances Hazardous to Health 2002 (COSHH)

## Slide 13: Waste Electrical and Electronic Equipment Directive (WEEE)
Waste Electrical and Electronic Equipment Directive (WEEE)
What is it?
WEEE is waste electrical and electronic equipment. It is end-of-life electrical and electronic equipment and covers virtually everything with a plug or battery. It is classed as either household or non-household
What is its purpose?
It is a regulation to oversea the requirements for the recovery, reuse, recycling, and treatment of waste electrical and electronic equipment

## Slide 14: Waste Electrical and Electronic Equipment Directive (WEEE)
Waste Electrical and Electronic Equipment Directive (WEEE)
What does it cover?
Large household appliances e.g. fridges, cookers, microwaves, washing machines and dishwashers
Small household appliances e.g. vacuum cleaners, irons, toasters and clocks
IT and telecommunications equipment – e.g. personal computers, copying equipment, telephones and pocket calculators
Consumer equipment e.g. radios, televisions, hi-fi equipment, camcorders ad musical instruments
Lighting equipment e.g. straight and compact fluorescent tubes and high intensity discharge lamps
Electrical and electronic tools – e.g. drills, saws and sewing machines, electric lawnmowers
Toys, leisure and sports equipment e.g. electric trains, games consoles and running machines
Medical devices e.g. (non infected) dialysis machines, analysers, medical freezers and cardiology equipment
Monitoring and control equipment e .g. smoke detectors, thermostats and heating regulators
Automatic dispensers e.g. hot drinks dispensers and money dispenser

## Slide 15: Restriction of Hazardous Substances Directive RoHS
Restriction of Hazardous Substances Directive RoHS
What is it?
Is a Directive aimed at eradicating certain hazardous substances from new electrical and electronic equipment (EEE).
Producers of EEE within the scope of the Directive are responsible for ensuring that their products meet the requirements of the Directive
What is its purpose?
To prevent hazardous substances from entering the production process and thereby keep them out of the waste stream.
What does it cover?
It is closely linked to WEEE, and restricts the use of the following ten substances:

## Slide 16: Restriction of Hazardous Substances Directive RoHS
Restriction of Hazardous Substances Directive RoHS
What does it cover?
It is closely linked to WEEE, and restricts the use of the following ten substances:
Lead(Pb)
Mercury(Hg)
Cadmium(Cd)
Hexavalent Chromium(Cr6+)
Polybrominated biphenyls(PBB)
Polybrominated diphenyl ether(PBDE)
Bis(2-ethylhexyl)phthalate(DEHP)
Butyl benzyl phthalate(BBP)
Dibutyl phthalate(DBP)
Diisobutyl phthalate(DIBP)

## Slide 17: Standards
What is a standard?
It is an agreed way of doing something. It could be about:
making a product
managing a process
delivering a service or
supplying materials
Standards can cover a huge range of activities undertaken by organizations and used by their customers.
The International Organisation for Standardisation (ISO) is one such standard made up of representatives from various national standards organisations.

## Slide 18: Standards
The International Organisation for Standardisation
The International Organisation for Standardisation (ISO) is one such standard made up of representatives from various national standards organisations.
In Knowledge Module 3 (Cloud Services), one of the standards mentioned was ISO 27001. Can you remember what this was?

## Slide 19: Standards
The International Organisation for Standardisation
The International Organisation for Standardisation (ISO) is one such standard made up of representatives from various national standards organisations.
ISO 27001 is a standard which provides a framework for the confidentiality, and integrity of information.
What is its purpose?
The purpose of a standard is to provide a reliable basis for people to share the same expectations about a product or service – in this example, security.

## Slide 20: Standards
What do they cover?
Organizations might use Standards for any of the following reasons:
a quality management standard to help them work more efficiently and reduce product failures
an environmental management standard to help reduce environmental impacts, reduce waste and be more sustainable
a health and safety standard to help reduce accidents in the workplace
an IT security standard to help keep sensitive information secure
a construction standard to help build a house
an energy management standard to help cut energy consumption
a food safety standard to help prevent food from being contaminated
an accessibility standard to help make buildings accessible to disabled users
an interoperability standard to ensure that bank and credit cards fit into ATMs and can be used throughout the world.

## Slide 21: Standards
ISO 27001 – Information Security Management System
According to its documentation, ISO 27001 was developed to "provide a model for:
establishing
implementing
operating
monitoring
reviewing
maintaining and
improving an information security management system.”

## Slide 22: Standards
ISO 27001 – Information Security Management System
An organisation must put in place the requirements of the standard and then apply for certification, which involves being audited to measure compliance.

## Slide 23: Standards
The process of continuous improvement is known as the Deming Cycle. If the result of the first cycle falls short of accreditation, the cycle can go through another iteration, and another, until the result is compliance with the standard.
https://en.wikipedia.org/wiki/PDCA

## Slide 24: Standards
ISO 27001 – Information Security Management System (ISMS)
Why pursue accreditation certification for ISO 27001 ISMS?
Accreditation demonstrates to existing and potential customers that an organisation has defined and put in place:
Best-Practice Information Security Processes
The benefits include the following:
The safeguarding of valuable data and intellectual property
The acquisition of new business and the retention of ones existing customer base
The avoidance of financial penalties and losses associated with data breaches
The protection and enhancement of ones reputation
The building of trust internally and externally
Compliance with business, legal, contractual and regulatory requirements
Satisfying audit requirements

## Slide 25: Standards
ISO 27001 – Information Security Management System (ISMS)
Why pursue accreditation certification for ISO 27001 ISMS?
The safeguarding of valuable data and intellectual property
The acquisition of new business and the retention of ones existing customer base
Reduces risk of data breach
Systematic approach to
  Identifying
  Managing
  Reducing the range of threats to which information is subjected
Conformity to the Standard can make the difference between winning and losing tenders
Expansion into global markets: ISO 27001 is a Legal requirement in India and Japan
Certification removes the need to complete detailed security questionnaires and respond to auditors for each new client

## Slide 26: Standards
ISO 27001 – Information Security Management System (ISMS)
Why pursue accreditation certification for ISO 27001 ISMS?
The avoidance of financial penalties and losses associated with data breaches
The protection and enhancement of ones reputation
Data breaches are:
  damaging to business
  excessively costly
ICO issued penalties > £5.5M for poor information security practices
Loss of customer confidence can have far more serious consequences for an organisation than the fines levied by the Information Commissioner’s Office (ICO) or the Payment Card Industry (PCI)
Cyber attacks are increasing in volume and strength daily, and the financial and reputational damage caused by an ineffectual information security posture can be fatal

## Slide 27: Standards
What is this?
(don’t worry, there is no reason why you should already know… )

## Slide 28: Standards
ISO 14000 - Environmental Management
What is it?
It belongs to a family of standards related to Environmental Management Systems
Provides practical tools for companies and organisations of all kinds looking to manage their environmental responsibilities.
Other family members include:
  14001 - specifies the requirements for an environmental management system that an organisation can use to enhance its environmental performance
  14004 - provides guidance for an organization on the establishment, implementation, maintenance and improvement of a robust, credible and reliable environmental management system
  14005 - provides guidance for all organisations, but particularly small- and medium-sized enterprises, on the phased development, implementation, maintenance and improvement of an environmental management system.
    It also includes advice on the integration and use of environmental performance evaluation techniques

## Slide 29: Standards
BS 18001- Occupational Health and Safety Management (OHSAS)
What is it?
An international standard which sets out the requirements for occupational health and safety management good practice for any size of organisation
It provides guidance to help you design your own health and safety framework – allowing you to bring all relevant controls and processes into one management system.
Following this standard helps an organisation demonstrate that they comply with Health & Safety legislation

## Slide 30: Standards
What do you think this might be about?

## Slide 31: Standards
BS 18001- Occupational Health and Safety Management (OHSAS)
What does it cover?
Legal requirements of Occupational Health and Safety Management
Compliance with applicable requirements
How to identify OH&S hazards and how to minimise health and safety risks
Makes sure all elements that are to manage health and safety effectively are clearly defined and clear processes put in place
Gives techniques to identify potential causes of accidents in the workplace
Helps you put in place procedures to reduce absenteeism
Requires you put in place clear processes for everyone to follow
Encourages active participation of the workforce with regards to the OH&S Management System
Ensures clear responsibility and accountability in the management system for OH&S
Further Reading: https://www.bsigroup.com/LocalFiles/en-GB/bs-ohsas-18001/resources/BS-OHSAS-18001-Features-and-Benefits.pdf

## Slide 32: Standards
BS EN 7671 - Requirements for electrical installations, IET Wiring Regulations
What is it?
It is the national standard in the United Kingdom for electrical installation and the safety of electrical wiring in:
domestic
commercial
industrial and other buildings
marinas or caravan parks
It helps an organisation demonstrate that they are compliant with the Electricity at Work Regulations 1989

## Slide 33: Standards
BS EN 7671 - Requirements for electrical installations, IET Wiring Regulations
What does it apply to?
It covers circuits supplied at nominal voltages up to and including 1000 volts AC or 1500 volts DC
The standard therefore covers the 230 volt 50 Hertz AC mains supply used in the UK for:
  Houses
  Offices and,
  Commerce

## Slide 34: Standards
BS EN 7671 - Requirements for electrical installations, IET Wiring Regulations
What does it cover?
Legal relationship and general requirements of BS EN 7671
Circuitry and Related Parts
Selection and setup of equipment
Earthing and bonding
Inspection, testing and certification
Further reading: https://tinyurl.com/y9ohlg62

## Slide 35: Standards
BS EN 7671 - Requirements for electrical installations, IET Wiring Regulations
Legal relationship and general requirements of BS EN 7671
Further reading: https://tinyurl.com/y9ohlg62
Covers such requirements as:
Key UK Legislation
The Electricity at Work Regulations 1989
The Electricity Safety, Quality and Continuity Regulations

## Slide 36: Standards
BS EN 7671 - Requirements for electrical installations, IET Wiring Regulations
Circuitry and Related Parts
Further reading: https://tinyurl.com/y9ohlg62
Covers such requirements as:
Principles and definitions
Circuit Design
  Voltage Drop
  Overload Protection
  Fault Protection
  Disconnection and electric shock
Parallel cables
RCDs and circuitry

## Slide 37: Standards
BS EN 7671 - Requirements for electrical installations, IET Wiring Regulations
Selection and setup of equipment
1 – Electromagnetic Compatibility
Further reading: https://tinyurl.com/y9ohlg62
Covers such requirements as:
Compliance with standards
Identification of conductors
Identification by colour
Wiring systems
EMC(1) cable separation – power, IT, data and control cables
Plugs and socket outlets
Ingress Protection (IP)

## Slide 38: Standards
BS EN 7671 - Requirements for electrical installations, IET Wiring Regulations
Selection and setup of equipment

## Slide 39: Standards
BS EN 7671 - Requirements for electrical installations, IET Wiring Regulations
Earthing and Bonding
Further reading: https://tinyurl.com/y9ohlg62
Covers such requirements as:
Protective conductors
Armoured cables as protective conductors
High Earth Leakage installations
Earthing conductors

## Slide 40: Standards
BS EN 7671 - Requirements for electrical installations, IET Wiring Regulations
Inspection, Testing and Certification
Further reading: https://tinyurl.com/y9ohlg62
Covers such requirements as:
Visual Inspection
Continuity testing
Insulation testing
Polarity testing
Prospective fault current testing
Overview of certificates and schedules
Completion of paperwork

## Slide 41: Standards
EN 50173/4 Information technology. Generic cabling systems. Homes
What is it?
It is a multi-subscribed-to standard that specifies a generic cabling for three groups of applications in homes:
Information and Communications Technologies (ICT)
Broadcast and Communications Technologies (BCT)
Commands, Controls and Communications in Buildings (CCCB)
If you are cabling up a new building, this standard covers everything you need to know to do it properly.

## Slide 42: Standards
EN 50173/4 Information technology. Generic cabling systems. Homes
Further reading:
What does it cover?
Current cabling standards as proposed collaboratively by:
The BSI (British Business Standards)
CENELEC - the European Committee for Electrotechnical Standardisation that is responsible for standardisation in the electrotechnical engineering field.
TIA /ANSI – Telecommunications Industry Association / American National Standards Institute
ISO – International Standards Organisation
Even though these bodies have equivalent standards for cabling, CENELEC produces the EN50173

## Slide 43: Standards
EN 50173/4 Information technology. Generic cabling systems. Homes
Further reading:
What does it cover?
EN50173 – 1 : Information technology - Generic cabling systems - Part 1: General requirements
EN50173 – 2 : Information technology - Generic cabling systems - Part 2: Office premises
EN50173 – 3 : Information technology - Generic cabling systems - Part 3: Industrial premises
EN50173 – 4 : Information technology - Generic cabling systems - Part 4: Homes
EN 50173-5, Information Technology – Generic Cabling Systems – Part 5: Data centres.
EN 50173-6, Information Technology – Generic Cabling Systems – Part 6: Distributed building systems.
TR 50173-99-1, Cabling guidelines in support of 10GBaseT.
TR 50173-99-2, Information Technology – Implementation of BCT applications using cabling in accordance with EN 50173-4.
TR 50173-99-3, Information Technology – Generic cabling systems – Part 99-3: Home cabling infrastructures up to 50m in length to support simultaneous and non simultaneous provision of applications.

## Slide 44: Standards
EN 50173/4 Information technology. Generic cabling systems. Homes
Further reading:
Environmental Classification (M.I.C.E)
EN 50173-1 Takes into consideration the following concept of Environmental classification when selecting cables
Whenever data cables (for example those that support 10/100BaseT traffic with a minimum cable spec of Cat 5) need to be installed, the engineer will need to take into consideration environmental factors. These factors could impact on the performance of the network.
Environmental factors to consider include the performance of the cable in a harsh high noise industrial environment.

## Slide 45: Standards
EN 50173/4 Information technology. Generic cabling systems. Homes
Further reading:
Environmental Classification (M.I.C.E)
Mechanical
Ingress Rating
Climatic and Chemical rating
Electromagnetic Rating
1 = Office, 2 = Light Industrial, 3 = Industrial
Ingress = Preventing things getting inside the cable

## Slide 46: Standards
EN 50173/4 Information technology. Generic cabling systems. Homes
Further reading:
Environmental Classification (M.I.C.E)
Analysis of M.I.C.E
M | I | C | E
Shock | Liquid | Temperature | ESD
Vibration | Particulates (i.e. soot) | Humidity | Radiated RF
Crush |  | Contaminates | Conducted RF
Impact |  | Solar Radiation | Transients
 |  |  | Magnetic Fields

## Slide 47: Standards
EN 50173/4 Information technology. Generic cabling systems. Homes
Further reading:
Environmental Classification (M.I.C.E)
The requirements of a higher class will continue to support those of a lower class. This means that E2 shall continue to operate under environmental conditions as E1.

## Slide 48: Standards
EN 50173 Information technology. Generic cabling systems. Homes
Further reading: https://www.bicsi.org/uploadedFiles/PDFs/Conferences/Greece/4-I2QS.pdf
Ref1: https://tinyurl.com/y7fp34ds
Ref2: 1 Two signals wires plus a separate ground wire to combat interference (RFI)
Classes for Balanced cabling(1)
Class | Channel Speed (Hz) | Cable category
A | Specified up to 0.1MHz | Cat 1 cable / connectors
B | Specified up to 1MHz | Cat 2 cable / connectors
C | Specified up to 16MHz | Cat 3 cable / connectors
D | Specified up to 100MHz | Cat 5e cable / connectors
E | Specified up to 250MHz | Cat 6 cable / connectors
EA | Specified up to 500MHz | Cat 6a cable / connectors
F | Specified up to 600MHz | Cat 7 cable / connectors
FA | Specified up to 1GHz | Cat 7a cable / connectors
I | Specified between 1.6GHz and 2.0GHz | Cat 8.1 (under development)
II | Specified between 1.6GHz and 2.0GHz | Cat 8.2 (under development)

## Slide 49: Standards
EN 50173 Information technology. Generic cabling systems. Homes
Ref1: https://tinyurl.com/y7fp34ds
Further reading: https://www.bicsi.org/uploadedFiles/PDFs/Conferences/Greece/4-I2QS.pdf
1 Two signals wires plus a separate ground wire to combat interference (RFI)
Structured Cabling architecture
Distances
The rules for the distances between the various sections of the Network channel state (in accordance with the EN 50173 standard), that the maximum horizontal channel (Service Distributor to Service Outlet) is a maximum of 100m (using a balanced copper cabling channel)

## Slide 50: Standards
EN 50173 Information technology. Generic cabling systems. Homes
Structured Cabling architecture
Imagine you are cabling up a new building. You need to run a series of long cables from the server room to each room in the building. What is the maximum distance of the cable you can run?

## Slide 51: Standards
EN 50173 Information technology. Generic cabling systems. Homes
Ref1: https://tinyurl.com/y7fp34ds
Further reading: https://www.bicsi.org/uploadedFiles/PDFs/Conferences/Greece/4-I2QS.pdf
1 Two signals wires plus a separate ground wire to combat interference (RFI)
Distances and architectures
EN 50173 states that the maximum length of a cable run should be no more than 100m in order to accommodate the minimum requirements of all ethernet cables.
However, don’t forget that the cables you route through the building have to be less than 100m in length. This is because there will be shorter patch cables on each end.

## Slide 52: Standards
EN 50173 Information technology. Generic cabling systems. Homes
Distances and architectures
However, don’t forget that the cables you route through the building have to be less than 100m in length. This is because there will be shorter patch cables on each end.
100m in total, unless active devices such as switches are used.

## Slide 53: Standards
EN 50173 Information technology. Generic cabling systems. Homes
Distances and architectures
Of course, a switch could be used at any point to regenerate the signal and extend the length – but it would not be best practice to fully cable a new building and depend on powered switches at various points.

## Slide 54: Standards
EN 50174 Installation technology. Cabling installation. Installation planning and practices outside buildings
What is it?
It is the European standard that specifies the basic requirements for the planning, implementation and operation of cabling using BALANCED (e.g. grounded) copper cabling and fibre optical cabling.
What does it cover?
• EN 50174-1, Information Technology – Cabling installation – Part 1: Installation specification and quality assurance
• EN 50174-2, Information Technology – Cabling installation – Part 2: Installation planning and practices inside buildings
• EN 50174-3, Information Technology – Cabling installation – Part 3: Installation planning and practices outside buildings
• TR 50174-99-1, Information Technology – Cabling installation – Remote Powering

## Slide 55: Standards
Codes of Practice – ITIL
Overview
What is it?
Definition: ITIL stands for Information Technology Infrastructure Library.
It Is essentially, a set of detailed practices for IT service management that focuses on aligning IT services with the needs of business. Put simply, ITIL is concerned with managing services within an IT environment.
Benefits to the organisation:
If everyone in an organisation is ITIL certified the benefit to a company is that processes and procedures are standardised across the business. This helps in ensuring a consistent best practice service across a business and improving outputs.

## Slide 56: Standards
Codes of Practice – ITIL
Overview
Benefits to the industry:
ITIL qualifications help to set benchmarks of quality across the IT industry. It's an adopted method across many mega-corps.
Benefits to the individual:
Being ITIL certified will provide an IT professional with effective IT skills that can be utilised across many organisations. It gives an individual ‘currency’ within the industry - Some employers request ITIL certification.

## Slide 57: Standards
Codes of Practice – ITIL
An Example related to an IT Helpdesk using the ITIL methodology:
A customer makes a call to log a fault.
The helpdesk agent takes the call, and records the details of the call.
The details and an incident number are logged.
A designated person who is the single point of entry reviews the log and then decides who is most suitable based on factors such as knowledge, and availability within the department.
Another person who is a single point of contact is then appointed to deal with that fault, and subsequently will continue to deal with that fault until it is either resolved or terminated. The customer will not be passed around to different call centre operatives.

## Slide 58: Standards
What is Energy Star?
Where have you seen this logo?

## Slide 59
Computers
Servers
Appliances
Heating and cooling systems
Home Electronics
Imaging Equipment
Lighting
Energy Star is an international standard for energy efficient consumer products. You may have seen the logo on a computer monitor or TV.
The Environmental Protection Agency in the US estimates savings of about $14 billion in 2006 alone.
It covers:
Standards

## Slide 60
Power supplies carrying the 80 Plus Bronze level or higher are Energy Star 4.0 compliant.
This means they are at least 80% efficient in the conversion of AC power to the voltages needed for PC components.
Standards

## Slide 61
When turned on, displays must draw less power than the maximum listed below. This depends on the resolution the monitor is working at.
There are also power specifications for sleep and off-mode.
Standards

## Slide 62
ASHRAE is the American Society of Heating, Refrigeration and Air-Conditioning Engineers.
Membership of this society means an individual is qualified to install or maintain these types of systems.
Standards

## Slide 63: Review
What is ITIL®?
A set of practices focusing on managing IT services, processes and resources to meet the needs of a business.
A set of practices that focuses on aligning IT services with the latest hardware software developments.
An internationally recognised guidebook of IT terminology used by industry to avoid mistakes in communication.
A computer programme for managing the hardware and software assets used in a business IT network.

## Slide 64: Review
What is ITIL®?
A set of practices focusing on managing IT services, processes and resources to meet the needs of a business.
A set of practices that focuses on aligning IT services with the latest hardware software developments.
An internationally recognised guidebook of IT terminology used by industry to avoid mistakes in communication.
A computer programme for managing the hardware and software assets used in a business IT network.

## Slide 65: Review
Which of the following tries to eliminate hazardous substances from the manufacturing supply chain?
WEEE
COSHH
RoHS
ASHRAE

## Slide 66: Review
Which of the following tries to eliminate hazardous substances from the manufacturing supply chain?
WEEE
COSHH
RoHS
ASHRAE

## Slide 67: Review
Which of the following deals with recycling of electronic equipment?
WEEE
COSHH
RoHS
ASHRAE

## Slide 68: Review
Which of the following deals with recycling of electronic equipment?
WEEE
COSHH
RoHS
ASHRAE

## Slide 69: Review
Which of the following specifies how cabling should be installed in buildings?
ISO 27001
ISO 14000
BS 18001
EN 50173/4
BS EN 7671

## Slide 70: Review
Which of the following specifies how cabling should be installed in buildings?
ISO 27001
ISO 14000
BS 18001
EN 50173/4
BS EN 7671

## Slide 71: Review
Which of the following specifies the colour of wires in electrical plugs?
ISO 27001
ISO 14000
BS 18001
EN 50173/4
BS EN 7671

## Slide 72: Review
Which of the following specifies the colour of wires in electrical plugs?
ISO 27001
ISO 14000
BS 18001
EN 50173/4
BS EN 7671